## Slide 1: Principles of Performance Engineering
Understanding CPU Microarchitecture for Software Optimisation

## Slide 2: Why Performance Engineering?
Understanding where your cycles go

## Slide 3: What is Performance Engineering?
The practice of measuring, analysing, and improving software performance
  Not guessing -- using hardware evidence to guide decisions
Modern CPUs are complex: multiple cache levels, out-of-order execution, speculative pipelines
  Source code alone cannot reveal where time is being wasted
Performance engineering answers two fundamental questions:
  Where is the program spending its time?
  Why is it spending time there instead of doing useful work?
Goal: convert more CPU cycles into useful computation
Profile
Diagnose
Fix

## Slide 4: The Modern CPU Pipeline
Instructions flow through a series of stages: Fetch, Decode, Execute, Retire
  Fetch: retrieve instructions from the instruction cache
  Decode: translate instructions into micro-operations
  Execute: perform the actual computation in execution units
  Retire: commit results to architectural state
Modern CPUs are superscalar: they can issue multiple micro-ops per cycle
  The pipeline has a fixed number of issue slots per cycle
Out-of-order execution: the CPU can reorder instructions for efficiency
  Instructions may execute in a different order than written in the program
  Cortex-M3 pipeline stages

## Slide 5: CPU Slots and Micro-Operations
A slot represents one opportunity for the CPU to make progress in a cycle
  Think of it as one place where a micro-op could have been issued
Every cycle, the CPU has a limited number of slots available
  Each slot either does useful work, or is wasted for a specific reason
Performance analysis asks: what happened to each slot?
  Did it produce useful work (Retiring)?
  Was the frontend too slow to supply work (Frontend Bound)?
  Was the backend stalled waiting for data (Backend Bound)?
  Was it spent on work later discarded (Bad Speculation)?
These four outcomes are mutually exclusive and account for every slot
  Slot Classification for Microarchitecture Analysis

## Slide 6: Top-Down Microarchitectural Analysis
A systematic method for diagnosing CPU bottlenecks

## Slide 7: The Top-Down Method
Start broad, then narrow: identify the dominant bottleneck category first
Every pipeline slot is classified into one of four buckets
  Frontend Bound, Backend Bound, Retiring, Bad Speculation
The bucket with the largest share of slots tells you where to investigate
  Then narrow down within that bucket to find the specific cause
This avoids wasting time optimising the wrong thing
  Always let the data guide the diagnosis, not intuition.
  Arm-Performix Microarchitectural Analysis

## Slide 8: The Four Buckets
Retiring: slots used for instructions that complete and produce useful results
  High Retiring = the CPU is converting capacity into real work
Frontend Bound: the frontend cannot supply micro-ops fast enough
  The backend could do more, but instructions are not arriving in time
Backend Bound: micro-ops arrived but cannot complete in the backend
  Usually waiting on data (cache misses) or busy execution units
Bad Speculation: slots wasted on work that gets discarded
  Commonly caused by branch mispredictions
  Arm-Performix Microarchitectural Analysis

## Slide 9: Frontend Bound
The frontend is the part of the CPU that fetches and decodes instructions
  It feeds the backend with a stream of micro-ops to execute
Frontend Bound means the instruction supply is the bottleneck
Common causes of frontend stalls:
  Instruction cache (I-cache) misses: code not in cache, must fetch from slower memory
  ITLB misses: virtual-to-physical address translation delays
  Complex or long instructions that take extra decode cycles
  Poor code layout causing frequent jumps across cache lines
  Front-end and Back-end division in an Arm “big” CPU

## Slide 10: Backend Bound
Memory Bound is the most common backend bottleneck
  Data not in L1 cache forces the CPU to wait for L2, LLC, or DRAM
  Each level is progressively slower: L1 ~4 cycles, L2 ~12 cycles, DRAM ~100+ cycles
Core Bound occurs when execution units are oversubscribed
  Too many instructions competing for the same functional unit
Reg
L1 Cache
L2 Cache
LLC Cache
DRAM
The backend executes micro-ops and accesses data from memory
Backend Bound splits into two sub-categories:
  Memory Bound: stalls caused by waiting for data from the memory hierarchy
  Core Bound: stalls caused by insufficient execution unit throughput

## Slide 11: Retiring
High Retiring with 0% SIMD means the CPU is busy but potentially inefficient
  Each instruction processes only one element instead of a vector
Retiring represents slots where instructions completed successfully
  High Retiring is good, but you can improve the type of work being done.
What type of instructions are retiring ?
  Integer operations (address calculations, loop counters)
  Scalar floating-point (one value at a time)
  SIMD / NEON (4 floats per instruction on Arm)
  SVE (up to 8 floats per instruction on Graviton3)
  Load and Store operations
  Cortex-A72 Microarchitecture

## Slide 12: Bad Speculation
Modern CPUs predict branches correctly over 95% of the time
  But in tight loops, even a small misprediction rate adds up
Bad Speculation is usually a small fraction of total slots
  If it is large, look at branch-heavy code with unpredictable patterns
Bad Speculation counts slots wasted on instructions that were discarded
The primary cause is branch misprediction:
  The CPU predicts which way a branch will go before knowing the answer
  If the prediction is wrong, all speculative work is thrown away
  The pipeline must be flushed and restarted from the correct path
  Difficult Speculative Execution

## Slide 13: The Narrowing Hierarchy
Top-down analysis works by progressively narrowing the diagnosis
Level 1: Which of the four buckets dominates?
  Frontend Bound, Backend Bound, Retiring, or Bad Speculation
Level 2: What is the sub-category within that bucket?
  Backend Bound narrows to Memory Bound or Core Bound
  Memory Bound narrows to L1, L2, LLC, or DRAM
  Retiring narrows to the instruction mix (scalar vs SIMD)
Level 3: Connect the specific metric to the software
  High L1D miss rate with strided access pattern? Restructure data layout
  High Retiring but 0% SIMD? Vectorise the hot loop or enable compiler optimisations.
Each level makes the diagnosis more precise and actionable
  Backend-bound Analysis

## Slide 14: Memory Hierarchy and Caches
How data movement dominates modern CPU performance

## Slide 15: The Memory Hierarchy
CPUs access data through a hierarchy of progressively larger, slower storage
  Registers: fastest storage, inside the CPU core
    Access time: ~1 cycle, size: a few KB
  L1 Cache: small and fast, closest cache to the core
    Access time: ~4 cycles, size: 32-64 KB per core
  L2 Cache: larger, shared or per-core depending on design
    Access time: ~12 cycles, size: 256 KB - 1 MB per core
  Last-Level Cache (LLC / L3): shared across cores
    Access time: ~40 cycles, size: 32-64 MB
  DRAM (Main Memory): large but slow
    Access time: ~100+ cycles, size: GBs
Performance depends on keeping frequently used data close to the core
Reg
L1 Cache
L2 Cache
LLC Cache
DRAM
  Faster
  Larger

## Slide 16: Cache Lines and Spatial Locality
The cache does not move individual bytes -- it moves cache lines
Spatial locality: if you access one byte, the whole 64-byte line is loaded
  Accessing neighbouring data is effectively free once the line is in cache
Temporal locality: data accessed recently is likely still in cache
  Reusing data before it gets evicted avoids expensive refetches
Strided access patterns defeat spatial locality:
  Jumping by N elements per iteration wastes most of each loaded cache line
  Only a fraction of each line is used before it is evicted = inefficient

## Slide 17: Measuring Cache Performance
MPKI: Misses Per Kilo-Instruction
  How many cache misses occur per 1,000 instructions executed
  Measured at each level: L1D MPKI, L2 MPKI, LLC MPKI
Miss Ratio: the fraction of accesses that miss at a given cache level
  L1D miss ratio of 50% means half of all data accesses miss in L1
Average Load Latency: how long loads take on average
  Includes hits and misses -- high values indicate poor cache behaviour

## Slide 18: Cache Line Utilisation
Cache line utilisation = bytes actually used / bytes loaded
  100% means every byte in the loaded line contributes to the computation
Low utilisation wastes memory bandwidth and cache capacity
  Unused bytes displace useful data from the cache
  The hardware prefetcher works harder for no additional benefit
Strategies to improve cache line utilisation:
  Restructure data layout (AoS to SoA) to separate hot and cold fields
  Tile loops so the working set fits in L1 or L2 cache
  Reorder loop nests to access data sequentially
  …

## Slide 19: Source Code Memory Optimisations: AoS vs SoA
Some, data layouts are more cache friendly than others
Array of Structures (AoS): one struct per element, all fields together
  struct Particle { float x, y, z, vx, vy, vz, mass, ... };
  Each struct may fill an entire cache line (64 bytes)
Problem: if the hot loop only uses a few fields, most of each line is wasted
  Using 24 bytes out of 64 = 37.5% cache line utilisation
Structure of Arrays (SoA): one array per field, all values contiguous
  float x[N]; float y[N]; float z[N]; float vx[N]; ...
  Every byte in each cache line is useful data for the hot loop
  AoS vs SoA

## Slide 20: Compute Efficiency
Getting more work done per instruction

## Slide 21: Scalar vs Vector (SIMD) Execution
Scalar: each instruction processes one data element
  One float multiply-add per cycle per instruction
SIMD (Single Instruction, Multiple Data): one instruction processes multiple elements
  NEON (Arm): 128-bit registers, processes 4 floats simultaneously
  SVE (Arm Graviton3): 256-bit registers, processes 8 floats simultaneously
A scalar loop leaves the vector units completely idle
  The CPU has hardware capacity that is simply not being used

## Slide 22: Instruction Mix Analysis
The Instruction Mix counts every retired instruction by type
  Integer, Scalar FP, NEON, SVE, Load/Store, Branch
For compute-heavy code, the Scalar FP vs SVE balance is key
  High Scalar FP + zero SVE = vector hardware is idle
Integer and Load dominance indicates overhead
  Address calculations, loop counters, and scalar loads per element
  Vectorised code amortises this overhead across a vector width
Always check instruction mix after applying a vectorisation fix

## Slide 23: The Optimisation Workflow
A repeatable process for performance engineering

## Slide 24: Profile, Diagnose, Fix, Re-profile
Step 1 -- Profile: collect hardware counter data on the unmodified workload
1
Step 2 -- Diagnose: identify the dominant bottleneck from the profile
2
Step 3 -- Fix: apply a targeted change that addresses the diagnosed bottleneck
3
Step 4 -- Re-profile: verify the fix worked as expected
4

## Slide 25: Key Takeaways
Performance engineering is measurement-driven, not guesswork
  Always profile before optimising -- fix the real bottleneck, not the assumed one
The Microarchitectural Analysis classifies every CPU slot into four buckets
  Frontend Bound, Backend Bound, Retiring, Bad Speculation
Memory hierarchy behaviour dominates most workload performance
  Cache misses, data layout, and working set size are critical
Instruction mix reveals whether vector hardware is being utilised
  Scalar code on SIMD-capable hardware leaves performance on the table
The optimisation loop: Profile, Diagnose, Fix, Re-profile
  Each iteration reveals the next bottleneck -- repeat until satisfied